## Slide 1: Cellular Automata Accelerator in RISC-V Processor
Callum Stew
3rd Year Project

## Slide 2: Presentation Structure
Background on Cellular Automata
Background on FPGAs, Verilog and RISC-V
Project Management
Hardware Implementation
Software Driver and Implementation
Results
Conclusion

## Slide 3: Cellular Automata
  Grid of cells in one or more dimensions with multiple states
  Simple rules dictate how a cells state changes on each iteration
  First used by Von Neumann in his Universal Constructor from 1966
  Wolfram extensively studied "elementary cellular automata“
  Conway's Game of Life (CGOL)
  Biham-Middleton-Levine Traffic Model[1]
  Disease Spreading Process[1]
  Forest fire modelling to find fire-fighting strategy effectiveness[2]
Images from: mathworld.wolfram.com/CellularAutomaton.html
Notes: Grid of cells in one or more dimensions
Multiple states
Simple rules dictate how states change
Used von neumann in 1966 (universal constructor 29 state)
Elementary cellular automata
Binary, one dimension, nearest neighbour
256 possible rules
binary, 2-dimensional, Moore Neighbourhood
Uses average - totalistic cellular automaton
Sum less than 2 or greater then 3 the cell is set to a state of 0
Sum exactly 3 the cell is set to 1
Traffic modelling Rule 184, BML Model
Disease spread
Forest fire model to simulate fire-fighting strategies

## Slide 4: Cellular Automata Acceleration
  Each cell can independently calculate its next state
  Inherently parallel process to calculate next step
  Excellent opportunity to exploit this using a hardware accelerator
  Greatly decreases time to compute large simulations allowing for faster development and testing of different situations
  Aim: Implement a hardware accelerator into a processor for basic cellular automata
Notes: Independently calculate next state
Inherent parallelism
Exploited using hardware
Greatly decrease computation time
Aim: implement accelerator

## Slide 5: FPGAs and Verilog
  An FPGA (Field Programmable Gate Array) is a semiconductor device based around a matrix of configurable logic blocks[3]
  The structure and configuration of these logic blocks are defined through register-transfer level (RTL) code to form any combinatorial or sequential logic
  Hardware Description Languages (HDL) such as Verilog are used to program the FPGA
  Allows for hardware to be developed and iterated on rapidly
  The Vivado software by Xilinx was used for this project
  Nexys A7-100T FPGA used for this project
Block Design
HDL Code
Behavioural Simulation
Synthesis
Implementation
Functional Verification
Bitstream
In Circuit Verification
Notes: Matrix of configuralble logic blocks
Restructured and configured with RTL code
Form any combinatorial or sequential logic
HDL Verilog
Rapid development
Nexys A7-100T board and Vivado
Development flow

## Slide 6: RISC-V
  Open standard Instruction Set Architecture
  Can be freely implemented by anyone allowing for wide adoption and modification
  Rocket Chip is an open-source System-on-Chip design generator that can produce synthesisable RTL
  Open-source project ‘vivado-risk-v’ used to generate a Rocket Core for the FPGA development board used
  A 64-bit single core processor was generated for this project due to the resource constraints of the FPGA used.
  AXI4 is an interface specification made by ARM
  Commonly used to connect custom hardware to the processor by making it available through virtual memory addresses
  Three types of interface: AXI4, AXI4-Lite, AXI4-Stream
Notes: Open-source Instruction Set
Implemented by anyone leading to wide adoption
Rocket chip gens synthesisable RTL
Vivado-risk-v uses rocket chip to generate core for the FPGA board used
64-bit single core
AXI4 interface standard ARM
Very commonly used
Vertial memory address
Three types

## Slide 7: Project Management
  Incremental development methodology using the inherent hierarchical design of the system
  Test driven development
  GitHub used for version control
  Kanban board used for tracking progress
  Weekly meetings with project supervisor to discuss progress
  Issues with the initial project idea was found as the Linux implementation for this project had functionality issues so bare metal code was used as an alternative
  Roughly followed the updated timeline from the progress report
Notes: Project followed a hierarchical design
Incremental development
Test driven dev
Github and kanban
Weekly meetings
Linux issues, bare metal
Roughly flowed update timeline in progress report

## Slide 8: Implementation – Block Design
  Hierarchy of modules
    AXI Register -> Board -> Cell
  Plan interfaces between modules
    AXI registers
    Board control signals
    Cell control signals
  Individual testing ensures that hard hardware is fully functional before build off from it.
AXI Lite Register
AXI Lite Interface
Board
Registers 0-65
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Board State Register
Cell 1 State
Cell 2 State
Cell 3 State
Cell 4 State
Cell 5 State
…
Notes: Conways game of life choses and rule set
Block design of overall project
Hierarchy
Plan interfaces/connections
Individual module testing

## Slide 9: Implementation – AXI
  AXI Lite standard used to interface with processor
    Up to 512 32-bit wide registers
    Does not support burst transfers
  Xilinx AXI Lite IP generator used to create the interface RTL
  Four Interactions need:
    Set initial state
    Read board state
    Send control signals
    Read if board has finished generating
  Flag needed when a value is set to the initial state or control registers
Image from: www.realdigital.org/doc/a9fee931f7a172423e1ba73f66ca4081
Notes: AXI Lite was used
Did not need greater then 32-bit registers or burst transfers
Xilinx generator used
Accelerator needed 4 interactions
Set initial state
Read state
Control signals
Check if finished
Modified to flag when a specific reg is set.

## Slide 10: Integration into RISC-V Processor
Notes: Connect the AXI interface clock and reset line
Assign the base address

## Slide 11: Implementation – Board
AXI Lite Register
AXI Lite Interface
Board
Registers 0-65
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Board State Register
Cell 1 State
Cell 2 State
Cell 3 State
Cell 4 State
Cell 5 State
…
  Interfaces with the registers set by the AXI interface
  Holds a register storing the state of every cell in the board
  Uses ‘generate’ block to instantiate the cell module
  Translates the command register to control signals
    Reset board
    Set new state
    Iterate n times
  Asserts response register
  O(1)
Notes: Interfaces with axi registers
Holds a reg for the board state, every cell can be simultaneously modified
Dynamically instantiates cell modules and assigns their x and y param
Runs command read from axi and set response reg

## Slide 12: Implementation – Cell – CGOL
  Pre-calculate neighbour indexes with ‘localparam’
  Retrieves the state from the board state register at calculated index
  Sums number of alive neighbours
  Sets next state of the cell
Notes: Localparams calculated at compile time to find neigboure indexes using the parameters X and Y
Every cell can view full board state and set its own cell state
Sets next state following rules

## Slide 13: Implementation – Wolfram Code
  Additional AXI Lite register used to hold the 8-bit Wolfram code
  Board is generated using only 1 dimension
  Cell calculates left and right neighbour indexes
  Checks which 3-bit pattern is matched
  Sets state to relevant bit from Wolfram code

## Slide 14: Testing
  Testbench simulates the AXI Write signals
  Sets the State of register 4
  Sends command to generate 30 iterations
Notes: All modules tested using testbench before being implemented on FPGA
Example shows seting a cell state and running 30 iterations

## Slide 15: Bare-metal Driver
  AXI Interface
    Struct with 32-bit ints defined at the AXI base address for the accelerator
    Each int points to the relevant address of the AXI Lite register
    This can be used to set the initial state, read state and send control signals
  Accelerator Test
    Get a time stamp by reading the machine cycle counter register
    Send the number of iterations to complete to the accelerator
    Busy wait on the response register getting set
    Get finish time stamp
  #define AXI_BASEADDRESS 0x6004000
  #define NUM_ITER 10
  typedef struct reg {
  volatile uint32_t reg_1;
  volatile uint32_t reg_2;
  } REG;
  REG * reg = (REG *)AXI_BASEADDRESS
  int done = 0;
  uintptr_t time_start;
  uintptr_t time_end;
  asm volatile ("csrr %0, 0xB00" : "=r" (time_start));
  reg->control = 15;
  while(!done) {
  if (reg->response) {
  asm volatile ("csrr %0, 0xB00" : "=r" (time_end));
  done = 1;
  }
  }
Notes: Bare metal c code run on processor
Interfcaes with the axi virtual memory address by creating a struct pointer at the base address
Use struct variables to interact with accelerator in this case setting it to iterate 15 times and waiting for the response reg to be set
To time how long it took the risk-v machine cycle counter is read using an assembly command

## Slide 16: Bare-metal Software Implementation
  Calculate Sum of Neighbours
    It first iterates over the board to find the number of alive neighbours for each cell
    Checks that the indexes are valid
    Writes sum to a different array
  Write new state
    Iterate over the board again assigning the new states
  O(2n2)
  int nvalid = (y-1)>=0;
  int evalid = (x+1)<32;
  int svalid = (y+1)<32;
  int wvalid = (x-1)>=0;
  int n = nvalid ? board[y-1][x] : 0;
  int e = evalid ? board[y][x+1] : 0;
  int s = svalid ? board[y+1][x] : 0;
  int w = wvalid ? board[y][x-1] : 0;
  int ne = nvalid && evalid ? board[y-1][x+1] : 0;
  int nw = nvalid && wvalid ? board[y-1][x-1] : 0;
  int se = svalid && evalid ? board[y+1][x+1] : 0;
  int sw = svalid && wvalid ? board[y+1][x-1] : 0;
  board_counts[y][x] = n+e+s+w+ne+nw+se+sw;
  if (board[y][x]) { // Alive
  if (board_counts[y][x] < 2 || board_counts[y][x] > 3) { board[y][x] = 0 }
  } else { // Dead
  if (board_counts[y][x] == 3) { board[y][x] = 1 }
  }
Notes: Written to different array as if it directly changes the cell it will cause future cells to be calculated incorrectly
Could be made more efficient by writing new state to a different bard then swapping the pointers in the variables holding the boards removing the need for the second full iteration of the board.

## Slide 17: Results
1 Iteration
  Accel: 158 clock cycles
  Soft: 325426 clock cycles
20 Iterations
  Accel: 158 clock cycles
  Soft: 6452393 clock cycles
1000 Iterations
  Accel: 1093 clock cycles
  Soft: 322508521 clock cycles
Chart: Clock Cycles
| 1 Iteration | 20 Iterations | 1000 Iterations
Accelerator | 158 | 158 | 1093
Software | 325426 | 6452393 | 322508521
Notes: 1, 20 and 1000 iterations
Logaritghimc scale used due to exponential decrease in time
1 and 20 iterations to same number of clock cycles as the bottle neck in the system is axi read time
About 26 iterations in one axi read
Could increase the clock speed of accelerator to allow for more iterations

## Slide 18: Results - Synthesis
Chart: Single Cell Resource Usage
| CGOL Cell | Wolfram Code Cell
LUT | 2 | 2
FF | 1 | 1
Chart: Resource Usage
| 32x32 CGOL | 1024 Wolfram Code | Processor
LUT | 6514 | 3906 | 49339
FF | 2145 | 2254 | 30890
Chart: 
| Processor | 32x32 CGOL | Unused
Total Resource Usage (LUT) | 77.82 | 10.27 | 11.91
Chart: Total Resource Usage (FF)
| Processor | 32x32 CGOL | Unused
Total Resource Usage (LUT) | 24.36 | 1.69 | 73.95
Notes: Wolfram code also implemented
Individual cells took same amount of resources
Board of 1024 cells had wolfram codes using less resources
Possible due to less neighbours allowing for optimisation of lut usage
Chart shows resources used overall of accelerator and processor

## Slide 19: Conclusion
  Completed the aim of this project by creating a functional accelerator providing significant decrease in calculation time.
  Using an AXI register connected directly to the processor it is relatively simple to the connect custom hardware allowing for easy adaption to any new cellular automata rule set.
  Maximum size of board is limited by FPGA resources
  Future Work
    Implement a more complicated rule set such as those described at the start
    Modify the Linux device tree and create a driver to allow use of the accelerator in Linux
    Use direct memory access to allow the accelerator to directly read and write a board state to memory allowing for larger boards to be split into sections which can be loaded into the accelerator without needed into do it manually in code.
Notes:   Completed all Specified functionality
  Worked Significantly faster than a software implementation
  Relatively simple to couple an accelerator to a risk-v processor using the AXI bus
  Maximum size limited by FPGA resources
Future work
  More complicated CA rule sets
  Linux driver

## Slide 20: Demo and Questions

## Slide 21: References
[1] – Li, X., Wu, J., Li, X. (2018). The Application Fields of Cellular Automata. In: Theory of Practical Cellular Automaton. Springer, Singapore. https://doi.org/10.1007/978-981-10-7497-4_8
[2] – K. Mutthulakshmi, Megan Rui En Wee, Yew Chong Kester Wong, Joel Weijia Lai, Jin Ming Koh, U. Rajendra Acharya, Kang Hao Cheong, Simulating forest fire spread and fire-fighting using cellular automata, Chinese Journal of Physics, Volume 65, 2020, Pages 642-650, ISSN 0577-9073, https://doi.org/10.1016/j.cjph.2020.04.001
[3] – Xilinx, AMD. What is an fpga?, https://xilinx.com/products/silicon-devices/fpga/what-is-an-fpga.html